## Slide 1: Computer Organization & Assembly Language
Lab 03
Introduction to IBM PC Assembly Language

## Slide 2
OBJECTIVES:
• Students will come to know the syntax of Assembly language.
• They will acquire knowledge on program data, variables and named constants.
• They will get to know about a few basic instructions of assembly language.
• Students will be able to Translate high-level language to assembly language.
• They will come to know about program structure of assembly language.

## Slide 3
Assembly Language Syntax
Statements are of two types: Instruction and Assembler Directive.
Statements can be written in the form: Name Operation_Field Operand(s)_Field Comment
Example: Instruction - START: MOV CX,5; initialize counter
Assembler directive- MAIN PROC
Name Field
Used for instruction labels, procedure names and variable names. Assembler translates name into memory address. Names can be 1 to 31 characters long and may consist of letters, digits or special characters. If period is used, it must be first character. Embedded blanks are not allowed. May not begin with a digit. Not case sensitive.

## Slide 4
Operation Field
Contains symbolic (Operation code). Assembler translates op code translated into machine language op code. Examples: ADD, MOV, SUB.
In an assembler directive, the operation field represents pseudo-op code. Pseudo-op code is not translated into machine code; it only tells assembler to do something. Example: PROC
pseudo-op is used to create a procedure.
Operand Field
Specifies the data that are to be acted on by the operation. An instruction may have zero, one or more operands. In two-operand instruction, first operand is destination, second operand is source. For an assembler directive, operand field represents more information about the directive. Examples: NOP, INC AX, ADD WORD1, 2.
Comment Field
Say something about what the statement does. Marked by semicolon in the beginning. Assembler ignores anything after semicolon. It is optional but a good practice.

## Slide 5
Program Data
Processor operates only on binary data. Data can be given as a number or a character.
• Numbers
• Binary
• Decimal
• Hexadecimal
• Characters
Named Constants
• Use symbolic name for a constant quantity
• Syntax:
name EQU constant

## Slide 6
Variables
• Each variable has a data type and is assigned a memory address by the program.
Possible Values:
• 8-bit Number Range: Signed (-128 to 127), Unsigned (0 to 255)
• 16-bit Number Range: Signed (-32,678 to 32767), Unsigned (0 to 65,535)
• ? - To leave variable uninitialized
Mainly three types
• Byte Variables
• Word Variables
• Others
• Arrays

## Slide 7
Pseudo - ops | Description | Bytes | Examples
DB | Define Byte | 1 | var1 DB ‘A’ array1 DB 10, 20,30,40
DW | Define Word | 2 | var2 DW ‘AB’ array2 DW 1000, 2000
DD | Define Double Word | 4 | Var3 DD -214743648
DQ | Define Quad Word | 8 | Var4 DQ ?
DT | Define Ten Bytes | 10 | Var DT ?
Data Defining Pseudo-Ops

## Slide 8
A Few Basic Instructions
• MOV
Transfer data between registers, between register and a memory location or move a number directly to a register or a memory location.
Syntax: MOV destination, source
Example: MOV AX, WORD1
• XCHG
Exchange the contents of two registers or register and a memory location. Syntax: XCHG destination, source
Example: XCHG AH, BL
• ADD
To add contents of two registers, a register and a memory location, a number to a register or a number to a memory location.
Syntax: ADD destination, source
Example: ADD WORD1, AX

## Slide 9
• SUB
To subtract the contents of two registers, a register and a memory location, a number from a register or a number from a memory location.
Syntax: SUB destination, source
Example: SUB AX, DX
• INC
To increment one to the contents of a register or memory location. Syntax: INC destination
Example: INC WORD1
• DEC
To decrement one from the contents of a register or memory location. Syntax: DEC destination
Example: DEC BYTE1
• NEG
To negate the contents of destination. Syntax: NEG destination
Example: NEG BX

## Slide 10
Statement | Translation | 
B = A | MOV AX, A MOV B, AX | 
A = 5 – A | MOV AX, 5 | 
 | SUB AX, A | 
 | MOV A, AX | 
 |  | OR
 | NEG A | 
 | ADD A, 5 | 
A = B – A | MOV AX, B SUB AX, A MOV A, AX | 
Translation of High-level Language to Assembly Language
• Consider instructions: MOV, ADD, SUB, INC, DEC, NEG
• A and B are two-word variables
• Translate statements into assembly language

## Slide 11
Model | Description
SMALL | Code in one segment, data in one segment
MEDIUM | Code in more than one segment, data in one segment
COMPACT | Code in one segment, data in more than one segment
LARGE | Both code and data in more than one segments. No array larger than 64KB
HUGE | Both code and data in more than one segments. Array may be larger than 64KB
Program Structure
• Machine programs consists of
• Code: Contains a program’s instructions.
• Syntax: .CODE name
• Stack: A block of memory to store stack
• Syntax: .STACK size
• Data: Contains all variable definitions
• Syntax: .DATA
Memory Models
• Determines the size of data and code a program can have.
• Syntax:
• .MODEL memory_model

## Slide 12
The Format of a Code
.MODEL SMALL
.STACK 100h
.DATA
;data definition go here
.CODE
MAIN PROC
;instructions go here
MAIN ENDP
;other procedures go here
END MAIN