## Slide 1: Computer Organization & Assembly Language
Lab 01
Microcomputer Systems

## Slide 2
Microcomputer Systems
OBJECTIVES:
• Students will be able to learn the components of microcomputer system.
• They will know how to execute an instruction.
• Students will have a brief knowledge about I/O devices.
• They will learn about various types of programming languages.
Components of a Microcomputer System
1. The CPU
CPU consists of these units units: Execution Unit (EU), Control Unit (CU), MMU and Bus Interface Unit (BIU).
Execution unit consists of Arithmetic and Logic Unit (ALU) and eight registers for storing data: AX, BX, CX, DX, SI, DI, BP and SP. It also contains FLAGS register.
Bus Interface Unit’s registers are: CS, DS, ES, SS and IP holding address of memory locations.

## Slide 3
2. Memory
Memory contents can be accessed either by byte or by word.
Byte is 8-bit and word is 16-bit.
Two operations can be performed on memory: read(fetch) and write(store).
Memory can be three types: RAM, ROM and Cache.
There are two types of RAM (Random Access Memory): DRAM: Dynamic RAM and SRAM: Static RAM.
ROM, EPROM, EEPROM, and FLASH memory are examples of ROM (Read Only Memory)
Cache is divided into two types: Internal Cache and External Cache.
3. I/O Ports
  There are two types of I/O ports: Serial Port and Parallel Port.
  Serial port transfers one bit at a time.
  Parallel port transfers 8 or 16 bits at a time.
  Examples of I/O ports are Magnetic Disk, Keyboard, Display Monitor and Printers.
  Magnetic disk is of two types: Floppy Disk and Hard Disk.
  There are three types of printers: Daisy Wheel, Dot Matrix and Laser.

## Slide 4
Buses
Processor communicates with memory and I/O devices by using signals that travel along a set of wires called buses. Three kinds of buses: address bus, data bus and control bus.
Instruction Execution (Fetch- Execution Cycle)
• Machine instructions have two parts: Opcode and Operands.
• The steps of executing an instruction are: Fetch and Execution.
Programming Languages
• Machine language: Example: 00100011
• Assembly language: Example: MOV AX, BX
• High Level Language: c = a + b

## Slide 5
Compiler
It is used to translate high level statement to assembly instruction(s) or machine instruction(s).
Assembler
It is used to translate assembly instruction to machine instruction
Mapping Between Assembly Language and High-Level Language
Instruction Class | C Language | Assembly Language
Data Movement | A=5 | MOV A,5
Arithmetic or Logic | B=A+5 | MOV AX, A ADD AX,5 MOV B, AX
Flow Control | goto LBL | JMP LBL

## Slide 6
Sample Math
Suppose a processor uses 20 bits for an address. How many memory bytes can be accessed?
Answer:
The number of memory bytes will be 220 = 1024x1024 = 1,048,576 = 1MB